## Slide 1: Lecture 3: Integrated assessment of climate change and sustainable development
Open-Source Energy System Modeling TU Wien, VU 370.062
Dipl.-Ing. Dr. Daniel Huppmann

## Slide 2: Required reading and preparation
SENSES Scenario Primer: www.climatescenarios.org/primer
D. Huppmann et al. (2018). A new scenario resource for integrated 1.5 °C research. Nature Climate Change, 8:1027-1030. doi: 10.1038/s41558-018-0317-4
  Paywall-free access at rdcu.be/9i8a

## Slide 3: The use of scenarios for policy analysis and the Intergovernmental Panel on Climate Change (IPCC)
Part 1

## Slide 4: A definition of climate change
The term climate change is about mean & variability and human activity
The Glossary – Annex 1 of the IPCC Special Report on Global Warming of 1.5°C (SR15).
Climate change Climate change refers to a change in the state of the climate that can be identified (e.g., by using statistical tests) by changes in the mean and/or the variability of its properties and that persists for an extended period, typically decades or longer. Climate change may be due to natural internal processes or external forcings such as modulations of the solar cycles, volcanic eruptions and persistent anthropogenic changes in the composition of the atmosphere or in land use. Note that the Framework Convention on Climate Change (UNFCCC), in its Article 1, defines climate change as: ‘a change of climate which is attributed directly or indirectly to human activity that alters the composition of the global atmosphere and which is in addition to natural climate variability observed over comparable time periods.’

## Slide 5: The impacts of climate change
Chart: 
| Habitat degradation | Crop yield change | Risk to power production | Water stress | Heatwave exposure
1.5°C | 91 | 35 | 334 | 3340 | 3960
2°C | 589 | 327 | 51 | 318 | 2026
3°C | 677 | 1455 | 357 | 262 | 1923
Source: “The hard truths of climate change — by the numbers“ (Nature 573:324, September 19, 2019) based on Byers et al. (2019, doi: 10.1088/1748-9326/aabf45)
Increasing temperatures exposes billions to multi-sector risks
Millions of people exposed

## Slide 6: The ”policy background” of climate change and sustainable development
Two landmark agreements in 2015 define the (research) agenda
“Transforming our world: the 2030 Agenda for Sustainable Development” was adopted at the United Nations Sustainable Development Summit on 25 September 2015. They comprise 17 Sustainable Development Goals (SDG) and 169 targets, which are measured with 232 indicators.
The „Paris Agreement“ was negotiated at the 21st Conference of the Parties (COP21) of the UNFCCC in Paris and adopted by consensus on 12 December 2015. It aims to keep global warming to “well below 2 °C” compared to pre-industrial levels while also to "pursue efforts to" limit the temperature increase to 1.5 °C.

## Slide 7: Definition of terms
There are numerous terms and concepts
  A forecast is based on assumptions of what is considered to occur most likely in the future
  A projection is based on hypothetical assumptions
  A scenario is a counterfactual development, usually compared to a baseline
  A pathway is a numerical evaluation of scenarios/projections combined with a narrative
Another way to think about this question: A scenario allows us to ask “what if” questions…
  Unfortunately, these definitions are just one possible set of usages. So beware, there is no consistent use of these terms in policy debate or scientific research!
It’s a challenge to talk about the future...

## Slide 8: The “hierarchy” of models and scenarios
The physical science basis: greenhouse gas concentration & radiative forcing
      The Representative Concentration Pathways (RCP)
Stylized climate models: emissions timeseries & temperature
Integrated Assessment Models (IAM): “optimal” balance between economy and mitigation
      Usually called “cost-benefit IAMs”
      Most famous example: the DICE model, 2018 Nobel Prize for William Nordhaus
Integrated Assessment Models (IAM): “optimal” transition pathway given a mitigation target
      Sometimes called “process-ased IAMs”
      The Shared Socio-Economic Pathways (SSPs)
    If you’re wondering about the difference between the two classes of IAMs: https://www.carbonbrief.org/qa-how-integrated-assessment-models-are-used-to-study-climate-change
Scenarios to analyze impacts and adaptation needs (that’s yet a different class of models)
It’s not quite obvious what we mean by “climate scenario”

## Slide 9: The Representative Concentration Pathways (RCP)
In IPCC AR5, scenarios were categorized by their radiative forcing at the end of the century as a proxy for temperature
This yields a range of emissions trajectories consistent with each RCP
Reference climate futures categorized by “radiative forcing”
Pathways of global GHG emissions in baseline and mitigation scenarios IPCC AR5 WG3 SPM.4 (Panel a)
IPCC, 2014: Climate Change 2014: Mitigation of Climate Change. Contribution of Working Group III to the Fifth Assessment Report (AR5)

## Slide 10: The Shared Socioeconomic Pathways (SSPs)
SSPs represent different futures assuming no climate policy
Each SSP has distinct assumptions about external drivers like population & GDP
Multiple IAMs implement all SSPs
  See Riahi et al. (2016) and Rogelj et al. (2017) for details
Not all SSP implementations are compatible with different levels of climate ambition
The SSPs allow to analyse climate policy relative to alternative futures
Schematic illustration of main steps in developing the SSPs, Fig. 1, O’Neill et al. (2017)

## Slide 11: Combining RCPs and SSPs
The name of the scenarios combine the SSP storyline (which assumes no climate policy) and the RCP target value (representing the ambition level of climate policy measures)
In the IPCC AR6 report, scenarios combining an SSP storyline and a RCP “climate ambition level” were used as benchmarks
Global surface temperature change by RCP-SSP, IPCC AR6 WG1, SPM 8, Panel a

## Slide 12: The gap between current policies and pledges to reduce emissions
Figure ES.6, UN Emissions Gap Report, 2021
Where do we stand in terms of (promised) emissions reductions?

## Slide 13: Historical temperature range and expected future heating
We are leaving the temperature range of human civilization
Historical global average temperature | IPCC AR6 WG1 SPM 1a
Stylized representation of expected temperature increases based on https://twitter.com/ClimateRsrc/status/1592084718321041409
1.0
2.0
3.0
°C
Goal of the Paris Agreement
Expected temperature increase based on announced policies (“pledges”)
Expected temperature increases based on currently implemented policies
1.5
2.5

## Slide 14: Definition of terms (2)
Process-based Integrated Assessment Models (IAM)
  Numerical tools to (primarily) evaluate scenarios of climate change mitigation
  They combine detailed representations of the human system (energy, economy) and the earth system (climate, oceans), including land use (and land use change)
  There is a broad range of methodological concepts underlying various IAMs, including (energy-system++) optimization, economic equilibrium (CGE), system dynamics
Many scenarios used in the IPCC assessment come from process-based IAMs

## Slide 15: A scenario primer
See www.climatescenarios.org/primer for more information
How can we use model-based scenarios to understand sustainable development?
The aim of SENSES is to generate tools for debate and deliberation of scenarios in the context of climate change mitigation and adaptation.
The interactive approach of co-production prevents that users become detached from the original scenario data, and minimizes the risk that information is misinterpreted and/or perceived as intransparent.
The Scenario Primer is the first in a suite of open tools developed in the SENSES project (senses-project.org).

## Slide 16: Criticisms of numerical (integrated assessment) models (I)
Frequent criticisms of large-scale numerical models for climate change
Closed and intransparent ’black box’ models
  Very sensitive to implicit assumptions and modeling artefacts
Over-optimistic assumptions on technological progress
  Assume availability of technologies like CCS, hydrogen economy
Use of discount rates: what’s the correct valuation of the future?
Not sufficiently focused on human development (too technocratic)
Virtually impossible to verify (projections of) input assumptions
  In contrast to climate models, where “backcasting” is frequently applied
“There is group-think in the modelling community”
There are many contentious aspects about numerical models of the economy-energy-environment-climate system

## Slide 17: Criticisms of numerical (integrated assessment) models (II)
  “IAM-based analyses of climate policy create a perception of knowledge and precision that is illusory, and can fool policy-makers into thinking that the forecasts the models generate have some kind of scientific legitimacy.”
  Robert S. Pindyck. "The Use and Misuse of Models for Climate Policy”. National Bureau of Economic Research (NBER), Working Paper No. 21097, 2015. doi: 10.3386/w21097
More importantly, projections based on numerical models may create a false impression of certainty and inevitability

## Slide 18: The big picture of IPCC assessments
Humans and Ecosystems
Physical Climate System
Scope of IPCC assessments
    Time scales:
      Paleoclimate to 2300 and beyond
    Spatial scales:
      Global to local
    Rates of change:
      Climatic & socio-economic developments
    Risks:
      To humans and ecosystems
The interaction between the human and earth systems
Based on lecture slides by Matthew Robbins, https://bit.ly/2Z3XJrt, presented at EGU 2019

## Slide 19: The big picture of IPCC assessments
Humans and Ecosystems
Physical Climate System
Based on lecture slides by Matthew Robbins, https://bit.ly/2Z3XJrt, presented at EGU 2019
The interaction between the human and earth systems
Emissions
Climate forcing
& processes
Mitigation
Hazards
Risks
Impacts
Adaptation

## Slide 20: The role and structure of the IPCC
The scientific assessment by the IPCC is structured in three working groups
Working Group I – The Physical Science Basis
      WG I assesses the physical science of climate change.
Working Group II – Impacts, Adaptation and Vulnerability
      WG II assesses the vulnerability of socio-economic and natural systems to climate change, negative and positive consequences of climate change and options for adapting to it.
Working Group III – Mitigation of Climate Change
      WG III focuses on climate change mitigation, assessing methods for reducing greenhouse gas emissions, and removing greenhouse gases from the atmosphere.
For each assessment report, a Synthesis Report is produced from the three WG contributions
Each contribution and the synthesis report has a “negotiated” Summary for Policy Makers
The IPCC provides policymakers with assessments of climate change, its implications and risks, and to put forward adaptation & mitigation options

## Slide 21: Principles of assessment by the IPCC
The IPCC assesses available scientific, technical and socio-economic literature relevant to understanding the scientific basis of climate change
  Published in peer-reviewed journals or eligible grey literature (e.g. IEA reports)
  In most cases, it is sufficient to extract relevant information, findings or data from manuscripts or reports
But relying only on published manuscripts & supplementary material for quantitative scenarios across studies is challenging
  Numerical results are not presented in the same data format
  Only a selection of numerical results presented in manuscript and SM e.g., only indicators of interest in relation to the research question
  Definitions and units differ across models and studies
The IPCC assesses the state of knowledge in the scientific literature; reports aren’t policy-prescriptive, but provide information to decisionmakers

## Slide 22: Collaboration between IPCC and the integrated assessment community
Adapted from Figure 2, Cointe, Cassen and Nadaï, Science & Technology Studies (forthcoming) sciencetechnologystudies.journal.fi/forthcoming/article/65031/40929
Over the past decade, the IPCC collaborated with the umbrella organization of global modelling teams to compile structured scenario ensembles

## Slide 23: A consolidated scenario resource for the IPCC assessment
Part 2

## Slide 24: The IAMC template for timeseries data
Over the past decade, the integrated-assessment community (IAMC) developed a tabular data format used for model inter-comparison projects
  High-profile use case: IPCC Fifth Assessment Report (AR5) see https://tntcat.iiasa.ac.at/AR5DB/
  Used by ~50 research teams around the world, for model inter-comparison projects, etc.
It’s not a great standard...
  No metadata, no sub-annual time resolution, bad scalability, ...
  But it’s easy to work with for non-experts, across platforms, ...
  And it’s the format we are stuck with in the IAM community...
A community effort for compiling and sharing scenario results
 | A | B | C | D | E | F | G | H | I | 
1 | Model | Scenario | Region | Variable | Unit | 2005 | 2010 | 2015 | 2020 | 
2 | MESSAGE | CD-LINKS 400 | World | Primary Energy | EJ/y | 454.5 | 479.6 | ... | ... | 
Notes: FAIR: Interoperable

## Slide 25: A scenario database for the IPCC AR5
For the IPCC’s Fifth Assessment Report (AR5), Working Group III, the Integrated Assessment Modeling Consortium (IAMC) and IIASA collaborated to compile a database of quantitative scenarios
This resource was used for the consistent assessment of emission pathways and system transitions in AR5
For AR5, the IPCC, IAMC and IIASA compiled a database to underpin the assessment of quantitative scenarios
IPCC, 2014: Climate Change 2014: Mitigation of Climate Change. Contribution of Working Group III to the Fifth Assessment Report
Figure SPM.4 (Panel a) | Pathways of global GHG emissions (GtCO2eq/yr) in baseline and mitigation scenarios

## Slide 26: Caveats of the IPCC AR5 scenario assessment
Measures to ensure transparency of the assessment and underlying data:
    Database publicly available for view and download: tntcat.iiasa.ac.at/AR5DB/
    Documentation of the scenarios: Krey, V., Masera, G., et al., 2014, Annex II: Metrics & Methodology. In: Climate Change 2014: Mitigation of Climate Change. Contribution of Working Group III to the Fifth Assessment Report
    Description of figure generation methods in supplementary material of the AR5
Shortcomings of the AR5 database in terms of usability and transparency:
      Scenario database is not state of the art for interactive web pages
      No intuitive citation for the data, and no acknowledgment for modelling teams as Annex or data authors (only references to their studies)
      Considerable effort required to reproduce figures and tables
      Treatment of scenario database as statistical sample by some researchers
The AR5 scenario database (2014) was a valuable resource for research, but it didn’t follow current best-practice principles of open science

## Slide 27: A new integrated 1.5°C scenario resource
An interactive scenario explorer launched for the SR15:
  data.ece.iiasa.ac.at/iamc-1.5c-explorer
Assessment and generation of figures & tables using open-source notebooks
  Categorization of scenarios for the assessment was implemented by the Chapter Scientist for the authors
  Development of the Python package pyam for analysis and visualization
Description of the process of compiling and assessing the scenario ensemble, including “do’s and don’ts”
  Commentary published in Nature Climate Change
Documentation of modelling frameworks and scenarios
  Details in the online scenario explorer and in an SR15 Annex
For SR15 (2018), we wanted to go one step beyond the efforts in AR5 for more transparency and reproducibility of the assessment
SR15, IPCC, 2018

## Slide 28: Scenario categorization for the SR15
Category | Subcategory | Probability | Number
Below 1.5°C | Below 1.5°C (I) | P1.5°C ≤ 0.34 | 0
 | Below 1.5°C (II) | 0.34 < P1.5°C ≤ 0.50 | 9
1.5°C return with low overshoot | Lower 1.5°C | 0.50 < P1.5°C ≤ 0.67 and P1.5°C(2100) ≤ 0.34 | 34
 | Higher 1.5°C | 0.50 < P1.5°C ≤ 0.67 and 0.34 < P1.5°C(2100) ≤ 0.50 | 10
1.5°C return with high overshoot | Lower 1.5°C | 0.67 < P1.5°C and P1.5°C(2100) ≤ 0.34 | 19
 | Higher 1.5°C | 0.67 < P1.5°C and 0.34 < P1.5°C(2100) ≤ 0.50 | 18
Lower 2.0°C |  | P2.0°C ≤ 0.34 (excluding above) | 74
Higher 2.0°C |  | 0.34 < P2.0°C ≤ 0.50 (excluding above) | 58
Above 2.0°C |  | P2.0°C > 0.50 during at least 1 year | 189
Based on Table 2.A.11, IPCC SR15, www.ipcc.ch/sr15/
The scenarios collected in the ensemble were categorized by their end-of-century (expected) warming and “temperature overshoot”

## Slide 29: The do’s & don'ts of scenario ensemble analysis
The scenarios were not designed to explore all possible developments; instead, they were compiled from a range of studies and reports.
  Don’t interpret the scenario ensemble as a statistical sample or in terms of likelihood or agreement in the literature.
  Don’t focus only on the medians, but consider the full range over the scenario set.
  Don’t cherry-pick individual scenarios to make general conclusions.
  Don’t over-interpret scenario results and don’t venture too far from the original research focus.
  Don’t conclude that the absence of a particular scenario (necessarily) means that this scenario is not feasible or possible.
Quoted from Box 1, Huppmann et al. (2018), Nature Climate Change 8:1027-1030. doi: 10.1038/s41558-018-0317-4
The scenarios form an unstructured “ensemble of opportunity”, so one must be careful when drawing conclusions from the data

## Slide 30: The IAMC 1.5°C Scenario Explorer
Visit the IAMC 1.5°C Scenario Explorer at https://data.ene.iiasa.ac.at/iamc-1.5c-explorer
Using predefined “workspaces” replicating SR15 figures for easy access
Notes: FAIR: Accessible

## Slide 31: The IAMC 1.5°C Scenario Explorer
Visit the IAMC 1.5°C Scenario Explorer at https://data.ene.iiasa.ac.at/iamc-1.5c-explorer
Socio-economic drivers across 1.5°C pathways (SR15 Figure 2.4)

## Slide 32: The IAMC 1.5°C Scenario Explorer
Visit the IAMC 1.5°C Scenario Explorer at https://data.ene.iiasa.ac.at/iamc-1.5c-explorer
Energy system transition in four illustrative pathways (SR15 Figure 2.15)

## Slide 33: IAMC 1.5°C Scenario Explorer
Visit the IAMC 1.5°C Scenario Explorer at https://data.ene.iiasa.ac.at/iamc-1.5c-explorer
The scenario explorer includes documentation of models, scenarios & variables

## Slide 34: A Python package for analysis and visualization of Integrated Assessment timeseries data
Part 3

## Slide 35: Comparing figures in the IAMC 1.5°C Scenario Explorer to the SR15
Range of assumptions in the predefined Scenario Explorer workspace and the SR15 (Figure 2.4, page 111)
Socio-economic drivers across 1.5°C pathways in the Scenario Explorer and the SR15 (Figure 2.4)

## Slide 36: The pyam package for IAM analysis & visualization
Harmonization and visualization of emissions pathways in IAMs
  aneris for IAM harmonization: software.ene.iiasa.ac.at/aneris
  pyam for plotting & visualization
    Scientific reference:
      Matthew J. Gidden et al. (2018) A methodology and implementation of automated emissions harmonization for use in IAMs. Environmental Modelling & Software 105:187-200. doi: 10.1016/j.envsoft.2018.04.002
Scenario assessment for the IPCC “Special Report on 1.5°C” (SR15)
  Completeness checks, data consistency validation, categorization
  Statistical analysis on filtered data and plotting figures for report
  Assessment and figures published together with the full report for transparency and reproducibility
  Implemented using best-practice of open, collaborative scientific software development
Joining forces across applications to develop a Python package
Notes: FAIR: Interoperable

## Slide 37: Scenario assessment for the IPCC
See all notebooks in a rendered format at data.ene.iiasa.ac.at/sr15_scenario_analysis
The scenario validation, categorization by warming outcome, and many SR15 tables and figures were implemented with pyam

## Slide 38: Scenario assessment for the IPCC
See all notebooks in a rendered format at data.ene.iiasa.ac.at/sr15_scenario_analysis
The scenario validation, categorization by warming outcome, and many SR15 tables and figures were implemented with pyam

## Slide 39: Distribution of scenario assessments via GitHub
$ git clone git@github.com:iiasa/ipcc_sr15_scenario_analysis.git
Feel free to clone and play around with the analysis notebooks!

## Slide 40: A suite of tools to work with 1.5°C scenarios
A new interactive online scenario explorer: data.ene.iiasa.ac.at/iamc-1.5c-explorer
  Recommended citation of the scenario explorer and data: D. Huppmann, E. Kriegler, V. Krey, K. Riahi, J. Rogelj, S.K. Rose, J. Weyant, et al. (2018) IAMC 1.5°C Scenario Explorer and Data hosted by IIASA. doi: 10.22022/SR15/08-2018.15429
Assessment and generation of figures & tables using Jupyter notebooks
  Rendered notebooks: data.ene.iiasa.ac.at/sr15_scenario_analysis
  GitHub repository: github.com/iiasa/ipcc_sr15_scenario_analysis
  Based on open-source package pyam: pyam-iamc.readthedocs.io
Description of the process of compiling and assessing the scenario ensemble, including “do’s and don’ts” D. Huppmann et al. (2018). A new scenario resource for integrated 1.5 °C research. Nature Climate Change, 8:1027-1030. doi: 10.1038/s41558-018-0317-4
Making it easy to dive into the IPCC scenario assessment
SR15, IPCC, 2018
Notes: DOIs

## Slide 41: Diving into the scenarios supporting the IPCC AR6
Short video on Youtube: https://t.ly/sbrL
The scenario ensemble supporting quantitative statements of the AR6 was compiled by the IAMC & IIASA on behalf of the IPCC similar to the SR15
Visit the AR6 Scenario Explorer and Database at http://data.ece.iiasa.ac.at/ar6
IPCC, 2022: Climate Change 2022: Mitigation of Climate Change. Contribution of Working Group III to the Fifth Assessment Report (AR6)

## Slide 42: The pyam package
Use cases and features
  Data processing Aggregation, downscaling, unit conversion, I/O to xlsx, csv & frictionless datapackage…
  Validation Checks for completeness of data, internal/external consistency, numerical plausibility …
  Analysis & visualization Categorization and statistics of scenario ensembles, plotting library, …
    Huppmann, Gidden, et al., 2021. Open Research Europe, 1:74 https://doi.org/10.12688/openreseurope.13633.2
A community package for scenario processing, analysis & visualization following best practice of collaborative scientific software development
#pyam_iamc
pyam-iamc.readthedocs.io
Notes: The

## Slide 43: Homework assignment
Browse through the AR6 Scenario Explorer
Analyse some salient aspect of the scenario ensemble, e.g.,
  Emission trajectories, energy system configuration, ...
  Possibly restricted to particular regions or economic sectors
  Possibly for particular models or projects (CD-LINKS, EMF33, ...)
Create a set of 3-4 figures/tables to illustrate your finding as well as some explanations
  As a Jupyter notebook using `pyam` create a new private GitHub repository, invite me as a collaborator when it is ready
  Invitation to collaborate due by Monday, April 24, 23:59
Replicate and extend some piece of assessment of the IPCC AR6